## Slide 1: Bug Algorithms

## Slide 2: Approach
Insects have only local knowledge
Even Stygmergy is local in space, though perhaps not in time.
Simple robots have similar constraints
The class of Bug Algorithms require local knowledge to accomplish some task.

## Slide 3: Bug Path Planning
Bugs know the direction to the goal (recall ants navigation via polarised light).
Bugs know the Euclidean distance between arbitrary points (not insect like).
Otherwise sensing is local (think range finders like an epuck and wheel encoders).

## Slide 4: Bug 0
Algorithm:
Repeat
Head toward goal
While path to goal is blocked
Follow obstacle edges
End while
End Repeat

## Slide 5: Bug 0
Algorithm:
Repeat
Head toward goal
While path to goal is blocked
Follow obstacle edges
End while
End Repeat

## Slide 6: Design obstacles to break Bug 0

## Slide 7: A Bug Trap
Algorithm:
Repeat
Head toward goal
While path to goal is blocked
Follow obstacle edges
End while
End Repeat

## Slide 8: Bug 0
The problem with Bug 0 was that is had no way to back track
Need to add some memory to the robot

## Slide 9: Bug 0
The problem with Bug 0 was that is had no way to back track
Need to add some memory to the robot

## Slide 10: Bug 1
Algorithm:
Repeat
Head toward goal
While path to goal is blocked
x := point where the obstacle was encountered
do
Follow obstacle edges all the way round
n := the minimum distance to the goal
while not back at x
go to n
End while
End Repeat
Lumelsky, V.J. & Stepanov, A.A.

## Slide 11: Bug 1
Algorithm:
Repeat
Head toward goal
While path to goal is blocked
x := point where the obstacle was met
do
Follow obstacle edges all the way around
n := the minimum distance to the goal
while not back at x
go to n
End while
End Repeat
n
n
x
x
Lumelsky, V.J. & Stepanov, A.A.

## Slide 12: Bug 2

## Slide 13: Bug 2
Algorithm:
While not at the goal
Follow the m-line
While path to goal is blocked
Follow obstacle edges
If m-line met then break
End While
End While

## Slide 14: Bug 2
Algorithm:
While not at the goal
Follow the m-line
While path to goal is blocked
Follow obstacle edges
If m-line met then break
End While
End While

## Slide 15: Debugging: Bug 2
Algorithm:
While not at the goal
Follow the m-line
While path to goal is blocked
Follow obstacle edges
If m-line met
then break
End While
End While
What went wrong?
What’s the fix?

## Slide 16: Bug 2
Algorithm:
While not at the goal
Follow the m-line
While path to goal is blocked
Follow obstacle edges
If m-line met closer to the goal
then break
End While
End While
Orange: Right Turning, Blue: Left Turning

## Slide 17: Bug 1 vs Bug 2

## Slide 18: Bug 1 vs Bug 2

## Slide 19: Bug 1 vs Bug 2

## Slide 20: Bug 1 vs Bug 2
Bug 1: Is exhaustive. Considers all choices
before progressing.
Bug 2: Is a greedy algorithm.
Takes the first thing that looks better.
Bug 2 will often outperform Bug 1,
but is less predictable.

## Slide 21: Tangent Bug

## Slide 22: Tangent Bug

## Slide 23: References
Robotic Motion Planning: Bug Algorithms, H. Choset, G.D. Hager, and Z. Dodds, Carnagie Mellon University, Robotics Institute 16-735
Lumelsky, V.J. & Stepanov, A.A., “Path-planning strategies for a point mobile automaton moving amidst unknown obstacles of arbitrary shape”, Algorithmica (1987) 2: 403